## Slide 1: Introduction to PCL - What can we do with point cloud data?
Seung-Chan Kim
March 18th, 2014
MAE683, Human Robot Interaction

## Slide 2: What is point cloud ?
A point cloud is a set of data points in some coordinate system.
Xtion PRO
Microsoft Kinect
…

## Slide 3: Example of point cloud data

## Slide 4: How to deal with the massive point clouds ?!
Notes: From scratch ? No !!!

## Slide 5: What is Point Cloud Library (PCL) ?
PCL is a large scale, open project for 3D point cloud processing
The PCL framework contains numerous state-of-the art algorithms including filtering, feature estimation, surface reconstruction, registration, model fitting and segmentation.
http://pointclouds.org/about/

## Slide 6: Who is developing PCL?

## Slide 7: The PCL framework contains numerous state-of-the art algorithms
Use Project MAE683-PCL, which contains essential examples of PCL

## Slide 9: PCD File I/O
PCD (Point Cloud Data) file format
Try
  01_pcd_read
  02_pcd_write
Loaded 10 data points from test_pcd.pcd with the following fields:
1.1 1.2 1.3
2.1 2.2 2.3
3.1 3.2 3.3
4.1 4.2 4.3
5.1 5.2 5.3
6.1 6.2 6.3
7.1 7.2 7.3
8.1 8.2 8.3
9.1 9.2 9.3
10.1 10.2 10.3

## Slide 10: Finding the K-nearest neighbors?
KdTree is used for finding the K nearest neighbors of a specific point or location
Try 03_kdtree_search !

## Slide 11: ICP(iterative closest point)
An algorithm employed to minimize the difference between two clouds of points.
ICP is often used
  to reconstruct 2D or 3D surfaces from different scans,
  to localize robots and achieve optimal path planning (especially when wheel odometry is unreliable due to slippery terrain),
  to co-register bone models, etc.
For more information
  http://www.asl.ethz.ch/education/master/info-process-rob/ICP.pdf
Notes: Saved 5 data points to input:
36.875 464.438 721.875
242.688 908.344 392.656
511.25 2.125 457
251.406 1006.72 278.875
691.656 842.875 307.969
size:5
Transformed 5 data points:
37.575 464.438 721.875
243.387 908.344 392.656
511.95 2.125 457
252.106 1006.72 278.875
692.356 842.875 307.969
has converged:1 score: 1.25615e-006
1 -1.59978e-007 -4.06864e-008 0.69922
-2.05472e-007 1 -1.21336e-008 -0.00158703
-8.47061e-007 -3.95886e-007 1 0.000396208
0 0 0 1
http://www.asl.ethz.ch/education/master/info-process-rob/ICP.pdf

## Slide 12: ICP(iterative closest point)
Notes: clc; close all; clear;
A=[
134.219 389.281 817.469
830.219 187.594 722.313
117.219 796.75 164.781
258.125 693.25 568
226.906 562.219 407.813
];
B = [
204.219 389.281 817.469
900.219 187.594 722.313
187.219 796.75 164.781
328.125 693.25 568
296.906 562.219 407.813
];
figure
plot3(A(:,1), A(:,2), A(:,3),'o');
hold on;
plot3(B(:,1), B(:,2), B(:,3),'ro');
grid;
xlabel('x');
ylabel('y');
zlabel('z')

## Slide 13
Try 04_iterative_closest_point

## Slide 14: Estimating Surface Normals in a PointCloud
05_estimating_sn
Notes: Surface normals are important properties of a geometric surface, and are heavily used in many areas such as computer graphics applications, to apply the correct light sources that generate shadings and other visual effects.

## Slide 15: Estimating “a covariance matrix” from a set of points is essential for estimating surface normals
Notes: http://pointclouds.org/documentation/tutorials/normal_estimation.php

## Slide 16
The solution for estimating the surface normal
=
an analysis of the eigenvectors and eigenvalues (or PCA) of a covariance matrix created from the nearest neighbors of the query point.
Estimating Surface Normals in a PointCloud

## Slide 17: Cutting off values that are either inside or outside a given user range
PassThrough filter - a simple filtering along a specified dimension
06_passthroughtest
0<z<200

## Slide 18: Downsampling a PointCloud using a VoxelGrid filter
./res/milk_cartoon_all_small_clorox.pcd
07_voxel_grid
Notes: http://www.pointclouds.org/documentation/tutorials/voxel_grid.php

## Slide 19: What Is a Voxel?
A voxel represents a value on a regular grid in three-dimensional space. Voxel is a combination of "volume" and "pixel" where pixel is a combination of "picture" and "element".
  a box, rather than a point, in space that has a volume

## Slide 20: Plane model segmentation: How to find all the points within a point cloud that support a plane model ?
08_plane_segmentation

## Slide 21: Plane model segmentation: How to find all the points within a point cloud that support a plane model ?
Loaded 307200 data points from test_pcd.pcd
Point cloud data: 307200 points
Model coefficients: 0.00601627 -0.821575 -0.570068 0.463954
Plane: 0.00601627x-0.821575y-0.570068z+0.463954=0
Model inliers: 196818
Notes: http://www.pointclouds.org/documentation/tutorials/planar_segmentation.php

## Slide 22: RANSAC for estimating parameters of a mathematical model from a set of data containing outliers
RANSAC (RANdom SAmple Consensus)
An iterative method that is used to estimate parameters of a meathematical model from a set of data containing outliers !
The RANSAC algorithm assumes that all of the data we are looking at is comprised of both inliers and outliers.
http://pointclouds.org/documentation/tutorials/random_sample_consensus.php
Notes: Fischler and Bolles in 1981
The input to the RANSAC algorithm is a set of observed data values

## Slide 23: RANSAC for estimating parameters of a mathematical model from a set of data containing outliers
The distribution of inliers can be explained by a set of parameters and a model. The outlying data does not fit the model.
http://pointclouds.org/documentation/tutorials/random_sample_consensus.php
Notes: Fischler and Bolles in 1981
The input to the RANSAC algorithm is a set of observed data values

## Slide 24: RANSAC for estimating parameters of a mathematical model from a set of data containing outliers
Plane with noise
Sphere with noise

## Slide 25: RANSAC for estimating parameters of a mathematical model from a set of data containing outliers

## Slide 26: Install and try the examples !
Put your stuff in the project named 12_openni_grabber !!!
http://robot.kaist.ac.kr/~kimsc/MAE683/example/
Notes: /home/kimsc/public_html/MAE683/example

## Slide 27: Thank you !

## Slide 28: Installation of PCL

## Slide 29
http://pointclouds.org/downloads/

## Slide 34
Notes: 10_random_sample_consensus.exe –f

## Slide 35
10_random_sample_consensus.exe

## Slide 36
10_random_sample_consensus.exe -f

## Slide 37
10_random_sample_consensus.exe -s